## Slide 1
Cortex-m4 for Anti-lock Braking System
Cortex-m4 Block Diagram
Microprocessor Features

## Slide 2: Architecture Rationale
Finite state machine of ECU controller in the ABS system.
Where:
S0 = inactive (brake not pressed),
S1=handellock,
S2= applyBrakePedal,
S3= pressureReduction,
S4= MonitorDeceleration and WL= WheelLocked.
• System Level Goals:
– G.1: Prevent wheel lockup during an emergency stop.
– G.2: Provide controlled stopping by maintaining maximum tire to road friction.
– G.3: Permit the driver to maintain steering while braking.
• Accident: The accident to be considered is the ABS vehicle crashes with a vehicle and the occupants are injured while ABS is involved.
• System Level Hazards:
– H.1: Loss of steering control during braking operation.
– H.2: ABS did not manipulate optimal wheel slip and stop in the shortest distance.
• Safety Constraints:
– ABS must engage automatically when rapid deceleration are detected.
– ABS must sense the motion of each wheel to detect a skid condition and be able to pulse the braking hundreds of times per second.
• Design Constraints:
– ABS must be engaged after brake pedal is pressed.
– ABS must prevent wheel lock-up in hard braking situations (e.g. when the speed of vehicle is over 15 mph) when lockup may occur.
• Design Requirements:
– ABS shall stop the vehicle in the shortest distance.
– ABS shall maintain the safe stop distance on loose road surface (e.g. snow-covered, gravel-roads, etc.).
• Functional Control Structure: Once the hazards to be evaluated have been reviewed, the safety analyst develops a control structure diagram of the system showing the control structure diagram which depicts the interacting control loop between ECU and HCU in ABS system.
Integrating State Machine Analysis with System-Theoretic Process Analysis
Asim Abdulkhaleq, Stefan Wagner
The control structure of ABS (ECU-HCU).

## Slide 3: Application Domain Features
Hardware interrupt (Braking Signal).
ADC (Wheel Speed Sensor).
ADC/DSP (Hydraulic Pressure Sensor).
DAC (Hydraulic Pressure Actuator Signal).
ABS architecture
Cyclic executive
  All tasks driven by one trigger (Braking pedal).
  Executed task depends on previous task’s results (deceleration rate, friction, wheel speed).
Busy-wait architecture
  No task executed until received triggering signal.
int main()
{
/* setup the interrupt service routine */
InitTasks();
RegisterTask(0, 30, FSMroutine, 1, 0);
/* enable interrupts */
while (true)
{
EnterLowPowerMode3();
}
return 0;
}
void Task2(void)
{
p = ReadPressure();
if (p > ThresholdP)
{
FSM = S3;
{
}
void Task1(void)
{
a = ReadRotation();
if (a > ThresholdA)
{
FSM = S1;
}
}
void FSMroutine(void)
{
Switch(FSM)
{
Case S1:
Task1();
break;
Case S2:
Task2();
break;
}
}